MECHANICAL SPRINGS

SHIGLEY: CHAPTER 10

Outline

- Springs General

  - Primary Function – Energy Storage

    - Material aspects

      - Area under the stress-strain curve is the work done/energy input per unit volume

      - For energy storage only the elastic portion is useful; the plastic region is only useful for energy absorption: “crumple zone”)

      - Therefore spring materials have very high yield stresses to maximize the energy storage potential

- Geometric aspects

  - A uniformly stressed part gives the highest energy storage for a given yield stress (example: a high yield strength rod or wire loaded in tension).

  - Stored energy in a rod:

At yield (σ = Sy ):

(best you can do)

Note: low modulus increases energy storage

  - Cantilever loaded at end (in bending)

At yield (σ = Sy ):

note much less than rod in tension

- Tapered cantilever example

b.  Springs

    - Torsion bar spring (circular) example

      - Maximum shear stress

T – torque applied

d – O D of rod

# Spring constant

where G = the shear modulus, l is the length., d is the O D of the rod

    - Helical compression spring (round wire)

      - Max. shear stress (including transverse shear )

where D is helix mean diameter and F is the applied

load

      - Max. shear stress corrected for curvature

where KB is correction factor for curvature and transverse shear

[Shigley approach]

With spring index C=D/d

Deflection (by Castigliano theorem)

Spring rate

  - Compression Springs

    - Types of ends: plain, squared or closed, squared & ground

    - Spring buckling (condition for stability)

Lo is the free length; α is the end condition constant (see table 10-2)

  - Spring Material

    - Spring materials are rated by ultimate tensile strength: although torsion yield is the issue in compression springs

    - Review spring material descriptions in table 10-3

    - Using the MDE for yield [] then for steels:

(eqn. 10-15)

Assumes Sy  is 60% -90 % of Sut .

- For high-tensile spring steels Samonov gives

(eqn. 10-16)

    - Some correlations of carbon steel springs give

**      (p.507)

    - Mechanical properties of some spring wires – see table10-5

    - For steel springs, use tabulated data for Ssy (Sut and % from tables 10-4 and 10-5) or if data is unavailable use equation above with **.

    - For small wire diameter springs with no temperature issues use music wire. Excellent, inexpensive material.

  - Helical Compression Design for static service

    - See figure 10-3 for process

    - Percent of tensile strength see table 10-6

    - Guide shown in example 10-1,2,3

  - Critical Frequency in helical springs

Natural frequency for springs between || plates

in radians/sec

where W is weight of active part of spring  (AL()

and ( is the specific weight

when one end is free

- The fundamental critical frequency should be ( 15 times the frequency of the force on the spring

  - Extension Springs – carry tension loads

    - In the body of the spring, use same equations for stresses as in compressive springs

    - May be wound to have a initial tension locked-in (see fig. 10-8)

    - Maximum torsional stress in the hook

where

is the minimum radius of hook

- See examples 10-6 and 10-7

  - Helical coil torsion springs

1. Torsion spring has bending induced in the coils, rather than torsion.

2.  Bending stress for a round-wire torsion spring:

where

and M  is the bending moment applied (Fr) and  is the spring index, as before, and d is the spring wire size

h. Spiral Torsion Spring  (Spring Motor)

- Other spring types

  - Belleville Springs (coned disk spring)

High load/low deflection springs

Unusual force deflection curve due to snap through

See fig. 10-12

  - Constant force springs (see section 10-14)

  - Volute Spring (see section 10-14)

  - Conical helical compression spring

    - Large change in spring rate with deflection

    - Applications for mounting compressors, etc.

  - Leaf spring (cantilever spring)

    - Heavy duty rear axel truck springs

    - Analyzed as a triangular shaped cantilever