ROLLING-CONTACT BEARINGS

Shigley: Chapter 11 [8th Edition]

Outline

- General

  - Sliding friction vs. rolling resistance

    - Demo of sliding friction  (f = 0.25)

    - Demo of rolling resistance – very low

    - Rigid Ball on a rigid flat surface (no deformation)

      - Neutral equilibrium  (no rolling resistance)

# Rolling resistance is related to deformation and roughness of ball or wheel and the surface

    - Contact stresses analysis gives equations for deformation of spheres and rollers on a flat surface

    - Rolling-contact bearings have very low rolling resistance at low loads

    - Criteria for a ball rolling or sliding on a surface

    - Rolling bearings have cyclic loading ( fatigue

  - Contact Stress Review

    - Equation of deformation of sphere on a flat plate

(3-68 modified*)

Where subscript 1 is the sphere and 2 is the flat plate

( is Poisson’s ratio and F is the contact load (*1/d2 = 0)

at z = 0.48a (

where z is the distance below the surface

- Example for the evaluating

  - Two spheres

  - Sphere on a flat surface

  - Ball-in-socket joint

    - Equation for deformation of a roller on a flat plate

(Eqn. 3-73*)

and

at z = 0.75b  (	  [*1/d2 = 0]

    - These equations assume no shear stress in the contact zone. Location of maximum shear stress

Sphere:  depth = 0.48a where a is the radius of the contact circle given by equation 3-68

Cylinder:  at a depth of 0.786 b where b is the half width of the contact band given by equation 3-73

Note: all principle stresses are compressive

Note: max. shear stress is below the surface in either case (this has implications as to failure mode).

- Rolling-Contact Bearings

  - Bearing types

    - Ball bearings

      - Figure 11-1: Cutaway of a ball bearing assembly

      - Figure 11-2: Various types of ball bearing mountings. Note: angular contact, self-aligning, thrust

    - Roller Bearings

      - Figure 11-3: Types of roller bearing mountings. Note spherical, thrust, and needle types

      - Other types of bearings

  - Bearing Life

    - Life is fatigue related so it’s stochastic in nature

    - Number of revolutions to evidence of fatigue

    - Hours of use at std. angular speed to evidence of fatigue

    - First evidence of fatigue not usually functionally limiting

    - Onset of fatigue failure --- Pit of area = 0.1 in2  ( gives a circle with a diameter of 3/8”.

  - Bearing Load Life at Rated Reliability

    - C10  - catalog load life rating (represents 10th percentile life rating) with 10^6 revs. or more (depends on manufacturer)

    - Equation relating desired load to catalog rating:

Where L’s are life in hours [LR rating; LD design req’t.]

n’s are speeds (revs/min)

FD is the desired radial load, lbf or kN

= 3 for ball bearings; or  = 10/3 for roller bearings

If you know the application, the catalog rating req’d is:

Eqn. (11-3)

See example 11-1

  - Bearing Survival: Reliability vs. Life

    - If the life measure is expressed in dimensionless form (x = L/L10 )

    - With a Weibull life distribution reliability can be expressed as

Eqn. (11-4)

Where R = reliability

x = life measure   L/L10   [L10   is the catalog life]

xo = minimum value of life measure (use 0.02)

- =  characteristic parameter corresponding to the 63.2121 percentile value of L/L10 (use 4.46)

b  =  shape parameter that controls the skewness in a Weibull distribution (use 1.483)

see figure 11-5 for a graphical reliability representation

The cumulative distribution function, F, can be written as:

Eqn. (11-5)

  - Relating Load, Life, and Reliability

    - Typically load, speed, and reliability aren’t as per the catalog

    - See figure 11-5 for this condition shown graphically

    - Determination of xD the design life multiple of std. catalogue life (usually 106 cycles but it can be more, depends on manufacturer)

(L10 usually 106)

    - Equation to find a catalog bearing load rating that is sufficient:

Eqn. (11-6)

- Examples

  - Bearing Reliability

Equation 11-6 can be solved for the reliability RD in terms of C10   the basic catalog rating of a selected bearing

Eqn. (11-18)

Where   ;

-application factor

  - Combined Radial and Thrust Loading

    - Ball bearings are able to carry some thrust load in addition to the major radial load (on the order of 35% without any loss of radial load rating)

    - The equivalent radial load Fe can be written

Eqn. (11-9)

= axial thrust load

= radial load

= equivalent radial load for catalog rating

= rotation factor (= 1 for inner race rotation; = 1.2 for outer race rotation)

where

and

See table 11-1 for values of X1, Y1, X2, Y2, and e

See figure 11-6 for graphical relationship of X and Y

  - Variable Loading

    - Bearing loads are often variable and occur in some identifiable pattern:

      - Piecewise constant loading in a cyclic pattern [Ex. 11-5]

      - Continuously  variable loading in a repeatable cyclic pattern [Ex. 11-6]

      - Random variation

    - See section 11-7 for combining various load histories to a single equivalent load history

  - Selection of Ball and Cylindrical Roller Bearing

    - See example 11-7

  - Selection of Tapered Roller Bearings

    - See example 11-8