SHAFTS AND AXLES

Shigley 8th edn. : Chapter 7

Outline

### Overview

### A	Definitions

    - Shaft – is a rotating member usually circular used to transmit power or motion. It provides the axis or rotation for elements such as gears, pulleys, flywheels, cranks, sprockets, etc.

    - Axle - is a non-rotating member that carries no torque and is used to support rotating wheels or pulleys. (Auto axle is a misnomer).

### B	Design Considerations Required in Shafting

  - Deflections and rigidity

      - Bending deflection

      - Torsional deflection

      - Slope at the bearings and shaft-support elements

  - Stress and Strength

      - Static strength

      - Fatigue strength

      - Reliability

      - Stability (Critical Speeds)

### Geometric Constraints in Shaft Design

### Step one – shaft material

        - Use a low carbon steel if possible

        - Deflection is modulus controlled (steel is steel)

          - No significant difference in modulus

- Step two – size the gears or pulleys

        - Consider speeds and power

        - Consider space for a keyway or torque transmitting element

        - Determine the forces/moments on the shaft

    - Step two – select bearings to provide adequate life for forces and speeds

        - Select bearings (Later chapters)

        - Determine distance between bearings

    - Step three  - consider shaft stresses

    - Step four – consider shaft deflections

- Strength Constraints

### Typically static stresses are not significant in shaft design because fatigue and critical speeds play a more important role in design. Since shafts rotate, there is a strong likelihood of fatigue issues.

    - Shaft Fluctuating Stresses – completely reversing due to rotation

Eqn. (7-3)

- Torsional Stresses – Steady state and alternating torsional stress

Eqn. (7-4)

    - Use equations 7-5 and 7-6 to get Maximum Distortion Energy, MDE equivalent stress

    - Use modified Goodman equation for fatigue analysis on a shaft

- Solve for the diameter, d (note: fortunately both bending and torsion have stress in terms of d3 )

- Using MDE Modified Goodman results in equations 7-7 for n and 7-8 for the diameter, d.

- Other fatigue criteria [eqns. 7-9 to 7-14]. We will use MDE Goodman.

    - See example7-1 for comparison of n with different criteria (Goodman will be the most conservative except for Soderberg)

- For more complete review see example 7-1 and 7-2

- The potential for yield must be checked

### Deflection Considerations – section 7-5

    - Deflection analysis requires complete geometric information

      - Forces and locations of gears and pulleys

      - Support locations, reaction loads, etc

    - Consider as beam deflection

      - With rotating shafts must have bearing supports

      - Bearings tend to act as simple supports to shaft; bearings offer support w/ low frictional resistance to rotation

    - See example 7-3 for deflection analysis

    - If deflection is too great at a location, the needed shaft diameter is given by equation (7-17):

Where nd is the design factor

And yall is the allowable deflection at that location.

- If slope is too great, use equation 7-18 to get a new diameter providing an acceptable slope:

Where (slope)all is the allowable slope.

- Determine dnew/dold and multiply all diameters by this ratio.

- Shaft Material

  - All steels have about the same Young’s modulus so rigidity can’t be controlled by material alone (only by geometry)

  - As usual, method of manufacture depends on volume

- Hollow Shafts

  - A hollow shaft can be used to reduce weight

  - Since the polar and bending moment of inertia are proportional to the 4th power of the diameter of a circular shaft and the cross sectional area is proportional to the 2nd power of the diameter, a hollow shaft can be designed to carry 90% of the torque capability of a solid shaft with much less weight

  - Example from handout

- Critical Speeds -  Section 7-6

  - Shaft design requires critical speeds that much higher than the anticipated operational speeds of the applications [Critical speed at least 2X operating speed]

  - Prime mover maximum speeds can be used as a guide to the required critical speeds for the shaft:

    - I C engines ………………………. ~7000 rpm (max)

    - Electric motors ………………….. ~ 1800 to 3600 rpm

    - Gas Turbine engine …………….. ~ 12,000 + rpm

    - See class notes and handouts for calculation of critical speeds

      - Basic equation

        - Shaft by itself

l is the length; A is X-sectional area; γ  is specific weight

E is Young’s Modulus and I is the moment of inertia; nc is the critical speed in rpm; g is the acceleration of gravity (32.2 ft/sec2or 386 in/sec2).

- Shaft with one element [Rayleigh’s method ]

Where nc is the critical speed in rpm; g is the acceleration of gravity (32.2 ft/sec2or 386 in/sec2); (st is the static deflection (ft. or in.).This is for a shaft with one element mounted on it, and the shaft is of negligible weight with respect to the element weight (often the case).

        - Example problem with one mass - see class handout

- Equation for shaft with multiple elements

or

Where wi is the ith element weight; (i is the total static deflection at the ith element location; g is the acceleration of gravity (32.2 ft/sec2or 386 in/sec2)

##### Equation for shaft with 2 elements; this equation reduces to

- Miscellaneous Shaft Components See section 7-7

Torque transfer elements

  - Keys

  - Splines

  - Setscrews

  - Pins

  - Press or shrink fits

Element location devices

  - Cotter pin and washer

  - Nut and washer

  - Sleeve

  - Shaft shoulder

  - Ring and groove

  - Setscrew

  - Split hub or tapered two-piece hub

  - Collar and screw

  - Pins

- See class notes

9.  Limits and Fits  -  see section 7-8

### Shaft Design Summary  - (for modification of an existing shaft)

  - Find the uniform-diameter shaft that meets the slopes and deflection at the bearings and power transmission elements

  - Consider the power transmission features: steps, shoulders, etc.

  - Using the approximate geometry, perform a deflection and slope analysis

  - Perform a strength analysis using MDE-Goodman theory.  Examine feature by feature the keyways, bearing shoulders, gear shoulder, etc.