BEVEL AND WORM GEARS

Shigley 8th: Chapter 15

Outline

### Bevel And Worm Gears

  - Bevel gears  -- Gear teeth are formed on a conical surface and are used mainly to transmit power with intersecting shafts. See figure 13-3.

  - Worm gears -- A worm gear set consists of a worm (resembling a screw thread) and the gear (a specialized helical gear) usually on shafts intersecting at 90 degrees. A worm gear gives very high gear reduction ratios. See figure 13-4.

### Bevel Gears

  - Types of Bevel Gearing

    - Straight bevel gears -- See figure 13-35 & 36. Simplest bevel gear. Used for power transmission on intersecting shafts for lower speed applications or when noise is not a consideration.

    - Spiral bevel gear  --  see figure 15-1.  The bevel counterpart of helical gears. Better for higher speeds where noise level is an important consideration.

    - Hypoid gears   -- Specialized spiral bevel gear used in automotive applications on drive shafts and differential gearing with the shafts offset (not intersecting). See figure 15 – 3.

  - Bevel gear stresses and strengths

    - Fundamental contact stress equations

      - U S customary Eqn. 15-1

      - S I units     Eqn. 15-1

See tables 15-1 and 15-2 for terms in equations

    - Permissible Contact Stresses

      - (U S Customary)		Eqn. 15-2

      - (SI Units)			Eqn. 15-2

    - Bending Stresses

      - (U S Customary)	Eqn. 15-3

      - (SI Units)		Eqn. 15-3

    - Permissible Bending Stress Equation

      - (U S Customary)	Eqn. 15-4

      - (SI Units)		Eqn. 15-4

  - See section 15-3 (pages 771 – 780) for determination of factors used in above equations

  - See figure 15-14 for “Road map” summary of bevel gear wear equations

  - See figure 15-15 for “Road map” summary of bevel gear bending equations

  - Straight Bevel gear analysis

    - See example 15 –1

  - Design of straight-bevel gear mesh

    - See example 15 - 2

### Worm gears

  - Worm Gearing  -- AGMA Equations

    - Crossed worm gears usually have a 90( shaft angle

    - Relation between shaft and helix angles

Equation 15 – 26

Where  is the shaft angle

Where P is pinion or worm; G is the gear

Plus sign for both helix angles are the same hand; minus sign when they are of opposite hand

    - The  worm gear diameter should fall in the following range:

Equation 15-27

Where C is the center (worm) to center (gear) distance

  - Worm Gear Analysis

- Worm gears have a much lower efficiency than other gearing systems

- Cooling can be a design constraint due to low efficiency. To reduce cooling load:

  - use multiple-thread worms

  - Keep worm pitch diameters as small as possible

- Self locking feature of worm gear drives – sometimes the gear cannot drive the worm (similar to self locking in threads).  To ensure worm gear will drive the worm:

Equation 15-56

- Worm gear set efficiency

  - When the worm drives the gear set

Equation `15-54

  - When the gear drives the gear set

- Worm tangential component Wwt   (in terms of the worm gear tangential component WGt  )

Equation 15-57

Where f is the coefficient of friction and λ is the lead angle

Without friction:

- Gear transmittal force in terms of output horsepower

Equation 15-58

where Ho  is the output horsepower; Ka  is the application factor;  nd  is the design factor;  VG  is the tangential speed of the gear

- The gear set frictional force

Equation 15-61

Where f is the coefficient of friction and λ is the lead angle

- The sliding velocity of the worm at the pitch cylinder V  is

Equation 15-62

- The friction power is

hp				Equation 15-63

  - Designing a worm-gear mesh

    - Read section 15-8

    - See example 15-4