FLEXIBLE MACHINE ELEMENTS

Shigley 8th: Chapter 17

Outline

### Belts

### A	General

    - Estimate, See Table 17-1 for the four principle types of belts

      - Flat

      - Round

      - “V” belts

      - Timing

    - Find Flat belt geometries – See figures 17-1 and 17-2

    - Variable speed belt drive – see figure 17-5

### B	See Class notes

### Flat and Round Belt Drives

  - Pulley Contact Angles

Eqn. 17-1

Eqn. 17-1

where D= diameter of the large pulley; d = diameter of the small pulley; C = center distance; ( = angle of contact

### Force and Torque on a pulley

Relation between tight and slack side tension

Eqn. 17-7

Eqn. 17-8

where F1 is the tight side tension; F2 is the slack side tension; Fc is the hoop tension due to centrifugal force; f is the coefficient of friction; and ( is the angle of wrap.

Eqn. 17-(e)

Where V = (dn/12 [ft/min]; w is the weight per unit length [lbf /ft]; g = 32.17 [ft/sec2]; d is the small diameter pulley [in]; and n is the rotation speed in rpm

      - The difference between F1 and F2 is related to the torque on the pulley

Where T = the torque; D = pulley diameter

- The tight and slack side tensions can be written

Eqn. 17-10

Eqn. 17-11

Where Fi is the initial tension; 	Eqn. 17-(i)

Which can also be written:

Eqn. 17-9

Note that if the initial tension is 0 then the torque transmitted is zero.

- The transmitted power

Eqn. 17-(j)

    - Steps in analyzing a flat belt

- Find exp (f() from belt geometry and friction

- From belt geometry and speed find Fc

- From T= 63025Hnom Ks nd/n find the necessary torque

- From torque T find the necessary (F1)a – F2  =2T/D

- Find F2

- From equation 17-(i) find the necessary initial tension, Fi

- Find the frictional development f’ < f. Use eqn. (17-7) solved for f’:

- Find the factor of safety from

    - The smaller pulley normally gives the limiting case for torque

    - See examples 17-1 and 17-2on flat belt pulleys

    - Flat metal belts see pages 883-885 and example 17-3

- V-Belts

### V-belts are able to provide more power transmission than flat belts

- For V-belts eqn. 17-7 becomes

Eqn. J&M 19-3a

where ( is one half the V-belt included angle [usually (=18(]

    - Gates Rubber Co equation for tight and loose side tensions

Eqn. 17-18

Where terms are the same as in eqn. 17-7.

Where Hd is the design power;Hnom is the nominal power; Ks  is the service factor from table 17-15.

Htab is the design power rating for certain conditions; it can be adjusted to other conditions with the following equation

Eqn. 17-17

where Ha is the allowable power/belt, table 17-12

K1 is the angle of wrap correction factor, table 17-13

K2 is the belt length correction factor, table 17-14

    - For V-belts the centrifugal tension is given by

Eqn. 17-20

where Kc is from table 17-16

- Power transmitted per belt based on  is

Eqn. 17-22

    - From equation 17-8 the largest tension is given by

Eqn. 17-23

Eqn. 17-24

    - The initial tension Fi

Eqn. 17-25

    - The factor of safety is

Eqn. 17-26

    - See example 17-4

### Timing Belts

    - See section 17-4

- Roller Chains

  - See section 17-5

  - Note equations: 17-29, 17-30, (b), (c), and (d)

  - Fatigue strength Power limitations for link plate and roller

    - Link plate – eqn. 17-32

    - Roller limited – eqn. 17-33

  - Center to center distance – eqn. 17-35 and eqn. 17-36

  - The allowable horsepower, Ha  -- eqn. 17-37

  - The required horsepower transmitted  -- eqn. 17-38

  - See Example 17-5

- Wire Rope

  - See section 17-6

  - Example 17-6

- Flexible Shafts

  - Read section 17-7