SPUR AND HELICAL GEARS

Shigley 8th : Chapter 14

Outline

- Background

  - Modes of gear failure

    - Bending stresses

    - Surface stresses

  - Bending Stresses – Lewis Bending Equation

    - Treating the gear tooth as a cantilever beam results in bending stresses (See figure 14-1)

# Eqn. 14-2

Where ( is the maximum bending stress at the base

the gear tooth. Wt   is the tangential force component on the end of the gear tooth; P is the diametral pitch; F is the gear tooth face width

# And 					Eqn. 14-3

# Y =(y where y is the Lewis form factor (see table 14-2 for values of Y).	 Where t is the base width; l is the length of the “cantilever”

    - Values of Y and y are determined from tables or charts

    - Assumptions

      - Ignores the radial component of the applied force

      - The maximum tooth occurs at the tip of the gear tooth

      - There is only one tooth engaged

  - Dynamic Effects – velocity effects

    - Barth equations – Kv for various gear materials and manufacturing process: equations 14-4a,b and 14-5a,b

    - Barth equations  -  Kv for SI units in equations: 14-6a,b and 14-7a,b.

    - Equation 14-2 adjusted for velocity factor

Eqn. 14-7

- The metric version

Eqn. 14-8

Where F and m are in mm; in Newtons gives  in Mpa

- Face width F should be 3 to 5 times the circular pitch p

- Example 14-1

  - Surface Durability --

    - Surface contact stresses applied to gears

Eqn. 14-11

Where is the surface compressive stress.

At the pitch lines of the teeth:

and

E’s are the Elastic constants of 1 and 2; F is face width

(’s are Poisson’s ratio; dp and dG are pitch diameters

    - AGMA elastic coefficient Cp

Eqn. 14-13

- Final compressive stress equation (including Kv)

Eqn. 14-14

- Minus sign since (C   is compressive

    - See example 14-3

  - AGMA Stress Equations

    - AGMA Bending stress equation 14-15

(U. S. Customary Units)

(S I Units)

Where Ko  is the overload factor; Ks  is the size factor;

Pd is the transverse diametral pitch; F(b) face width of narrower gear; Km (KH  ) load distribution factor; KB  is the rim-thickness factor; J (YJ ) is the geometry factor for bending strength (including root fillet stress concentration factor).

    - AGMA Pitting Resistance Equation (contact stresses) 14-16

(U. S. Customary Units)

(S I Units)

Where Cp (ZE) is an elastic coefficient,

Cf (ZR) is the surface condition factor;

dp  (dw1 ) is the pitch diameter of the pinion, in. (mm)

I  (Zl ) is the geometry factor for pitting resistance

- Factors explained in later sections

- AGMA Strength Equations

      - AGMA Allowable Bending Stress (Equation 14-17)

(U. S. Customary Units)

(S I Units)

- AGMA Allowable Contact Stress (Equation 14-18)

(U S Customary Units)

(S I Units)

() are the allowable contact stresses lbf/in2 (N/mm2)

ZN  Stress cycle life factor

CH (ZW) are the hardness ratio factors for pitting resistance

KT (Y() are the temperature factors

KR (Y Z ) are the reliability factors

SH  is the AGMA factor of safety, a stress ratio

- Values of  are shown in figure 14-5 and tables 14-5 and 14-6

  - Geometry Factors I and J  (ZI and ZJ)

    - For Spur gear J factors see figure 14-6

    - For Helical gear J factors see figure 14-7 and 14-8

    - Surface geometry factors I   (Z  )

(external gears)  Eqn. 14-23

(internal gears) Eqn. 14-24

Where   		Eqn. 14-22

and  from Eqn 14-21( is 1 for spur gears)

Eqn. 14-21

Where Z is given by eqn.14-25

  - The Elastic Coefficient  CP ( ZE)

    - See table 14-8

  - Dynamic Factor Kv

    - Use figure 14-9

  - Overload Factor Ko

  - Surface Condition Factor   -- Use 1

  - Size factor Ks

    - Load Distribution Factor Km  (KH )

        - See section 14-11

  - Hardness Ratio Factor  CH

    - See figures 14-12 and 14-13

  - Stress Cycle Life Factors Y  and Z

    - See figures 14-14 and 14-15

  - Reliability Factor KR (YZ )

- Table 14-10

  - Temperature Factor KT ( Y( )

    - Use    KT ( Y( )  =1.0

  - Rim Thickness Factor  KB

    - Backup Ratio

      - See figure 14-16

    - Rim Thickness Factor  Eqn 14-40

  - Safety Factors  SF  and SH

    - Definition of

    - Definition of

  - Analysis

    - See figure 14-17: Road map for Spur gear bending

    - See figure 14-18: Road map for Spur gear wear

    - Example 14- 4

    - Example 14-5